## Slide 1: SCSI Pass-Through (SPT) Update (TOI) by Robin T. Miller Robin.Miller@gmail.com
Updated: September 23rd, 2025

## Slide 2: Agenda
Short History
What is SPT?
Why use this SPT Tool?
SPT Features
SPT Roadmap
Q&A

## Slide 3: Short History (mine, leading up to SPT)
Started working with pSCSI in 1986 @Compugraphic
Wrote SCSI subsystem (HBA, disk, tape drivers) for System V
Developed streaming SCSI Tape driver for Solaris
Enhanced Solaris format utility with extended SCSI commands
Member of Tru64 SCSI/CAM (Common Access Method) team
  Developed IOCTL interfaces, configuration code, tape library driver
Developed SCSI CAM Utility (SCU) for Tru64 Unix @DEC
  Ported SCU to multiple OS’s for DEC Data Products Group
Started developing SCSI pass-through (SPT) in 2006 @NetApp

## Slide 4: SCSI Pass-Through (SPT) Utility
SPT allows SCSI testing via the SCSI pass-through API
  This is an OS specific user level API for issuing SCSI operations.
Supported on most OS’s, except OSX (lacks SCSI API)
A fair amount of code originated from DT tool
SPT is open source, and is available on GitHub:
  https://github.com/RobinTMiller/spt
    Note: Github does NOT include vendor extensions.
Storage Enclosure Services (SES) support added

## Slide 5: Why Use This SPT Tool?
Advanced Testing Requires Advanced Test Tools
Key SPT Features: (one tool versus many)
  Specifically designed for SCSI testing
  Supports multiple jobs/threads for high load & stress
  Supports JavaScript Object Notation (JSON)
Useful for developers, automation, and support.
This TOI will hopefully whet your appetite!
We have internal developer (Robin) and support! 

## Slide 6: SPT Features
Send/Receive Diagnostic Support (added for SES pages)
Support for I/O Ranges (for read/write/verify operations)
Support for I/O Modes (copy/verify/mirror operations)
Support for Multiple Slices (threads for higher load & stress)
Triage/Recovery Support (detailed errors, recovery, etc)
Extended SCSI CDB Support (encode/decode CDB’s)
Enhanced Script File Support (custom test scripts)
Emit Status Control Strings (roll your own output format)
Test Check / Expect Options (automatic data/sense checks)
Provides ASCII and JSON output formats! (work-in-progress)
Support to unpack SCSI data (decode data in user format)

## Slide 7: SPT Command Format
Basic Command Format:
# spt dsf=device cdb=‘hh hh …’ dir={none|read|write} length=value pout=“hh hh …” threads=value …
  dsf is the device special file, e.g. /dev/sdXX or /dev/sgXX or /dev/dmXX (SCSI device)
  cdb = the Command Descriptor Block hex bytes (use ‘spt showopcodes’ to see operation codes)
  dir = the data direction (defaults to ‘none’)
  length = the data length
  pout = the parameter out data (optional)
  threads = the number of threads (optional, defaults to 1)
Short Hand Commands: (for ease of use)
# spt dsf=/dev/sg42 showhelp <- SES PP Help page
versus
# spt dsf=/dev/sg42 cdb="1c 01 03 ff ff 00" dir=read length=65535 sname="Receive Diagnostic"
I/O Parameters also Simplify CDB Generation:
# spt dsf=/dev/sdl cdb=0x88 bs=64k starting=0 limit=1g slices=10 (READ (16) of 64k to limit of 1g of data)

## Slide 8: Send/Receive Diagnostic Support
Options Added for Storage Enclosure Services
  Storage Enclosure Services (SES) Specific Options:
  element_index=value The element index. (or element=)
  element_tcode=value The element type code. (or etcode=)
  element_scode=value The element status code. (or escode=)
  element_type=string The element type. (or etype=)
  element_status=string The element status. (or estatus=)
  rcvdiag Issue a receive diagnostic command.
  senddiag Issue a send diagnostic command.
  showhelp Show enclosure help text diagnostic page.
  Examples:
  # spt rcvdiag page=configuration

## Slide 9: Diagnostic Page Codes/Names
Added Specifically for Storage Enclosure Devices
# spt logprefix= rcvdiag page= (pages in green support decode functions)
  Diagnostic Page Codes/Names:
  0x00 - Supported (supported)
  0x01 - Configuration (configuration)
  0x02 - Enclosure Control/Status (enclosure)
  0x03 - Help (help)
  0x04 - String In/Out (string)
  0x05 - Threshold In/Out (threshold)
  0x07 - Element Descriptor (element)
  0x08 - Short Enclosure Status (short_enclosure)
  0x09 - Enclosure Busy (enclosure_busy)
  0x0a - Additional Element Status (addl_enc_status)
  0x0b - Subenclosure Help Text (subenc_help_text)
  0x0c - Subenclosure String In/Out (subenc_string)
  0x0d - SES Diagnostic Pages (ses_diagnostic)
  0x0e - Download Microcode Control/Status (download)
  0x0f - Subenclosure Nickname Control/Status (subenc_nickname)

## Slide 10: Storage Enclosure Services (SES) Pages
SES Pages Supported Today:
  0x00 = supported pages
  0x01 = configuration
  0x02 = enclosure status
  0x03 = help text (showhelp)
  0x04 = string in status
  0x07 = element descriptors
  0x0a = additional element status
  0x0e = download microcode
Two output formats supported:
  ASCII format (default)
  JSON format (added for automation)

## Slide 11: Supported Diagnostic Pages
# spt rcvdiag page=supported
Diagnostic Pages Supported:
Supported Page (Code = 0x00)
Configuration Page (Code = 0x01)
Enclosure Control/Status Page (Code = 0x02)
Help Page (Code = 0x03)
String In/Out Page (Code = 0x04)
Threshold In/Out Page (Code = 0x05)
Element Descriptor Page (Code = 0x07)
Additional Element Status Page (Code = 0x0a)
Download Microcode Control/Status Page (Code = 0x0e)
Tag Data In/Out Page (Code = 0x10)
Mini SAS HD Cable VPD Page (Code = 0x17)
#

## Slide 12: SES Configuration Page (PP Enclosure)
# spt rcvdiag page=config logprefix=
Configuration Diagnostic Page:
Page Code: 0x1
Number of Secondary Enclosures: 0
Page Length: 244 (0xf4)
Generation Number: 0
Enclosure Descriptor List:
Number Enclosure Services Processes: 1
Relative Enclosure Services Process ID: 1
Subenclosure Identifier: 0 (Primary)
Number of Type Descriptor Headers: 10
Enclosure Descriptor Length: 36 (0x24)
Enclosure Logical Identifier: 0x5000ccab00ff0108
Vendor Identification: HGST
Product Identification: STOR ENCL JBOD
Product Revision Level: 0116
Element Type: Array Device Slot (0x17)
Number of Elements: 98
Subenclosure Identifier: 0 (Primary)
Text Length: 16 (0x10)
Element Text: 'Array Slots '
...

## Slide 13: SES Configuration Page (JSON format)
# spt rcvdiag page=config output-format=json logprefix=
{
"Configuration": {
"Length": 8,
"Offset": 0,
"Bytes": "01 00 00 f4 00 00 00 00",
"Page Code": "0x01",
"Secondary Enclosures": 0,
"Page Length": 244,
"Generation Number": 0,
"Enclosure Descriptor List": [
{
"Length": 40,
"Offset": 8,
"Bytes": "11 00 0a 24 50 00 cc ab 00 ff 01 08 48 47 53 54 20 20 20 20 53 54 4f 52 20 45 4e 43 4c 20 4a 42 4f 44 20 20 30 31 31 36",
"Enclosure Services Processes": 1,
"Reserved (byte 0, bit 3)": 0,
"Reserved (byte 0, bit 7)": 0,
"Subenclosure Identifier": 0,
"Type Descriptor Headers": 10,
"Enclosure Descriptor Length": 36,
"Enclosure Logical Identifier": "0x5000ccab00ff0108",
"Vendor Identification": "HGST ",
"Product Identification": "STOR ENCL JBOD ",
"Product Revision Level": "0116"
}
],
...

## Slide 14: SES Element Descriptor Page with Debug
# spt rcvdiag page=element enable=Debug logprefix=
Element Descriptor Diagnostic Page:
Length: 8 (0x8)
Offset 0 (0x0): 07 00 16 32 00 00 00 00
Page Code: 0x7
Reserved (byte 1): 0
Page Length: 5682 (0x1632)
Generation Number: 0
...
Element Location: 230
Length: 4 (0x4)
Offset 4966 (0x1366): 00 00 00 38
Element Descriptor: 0
Element Text: IOM
Reserved (byte 0): 0
Reserved (byte 1): 0
Descriptor Length: 56 (0x38)
Index: 00 01 02 03 04 05 06 07 08 09 10 11 12 13 14 15
Offset 4970 (0x136a): 45 53 43 45 20 49 4f 4d 20 20 20 20 20 20 20 20
E S C E I O M
Index: 16 17 18 19 20 21 22 23 24 25 26 27 28 29 30 31
Offset 4986 (0x137a): 31 45 42 30 30 35 30 2d 33 41 20 20 20 20 20 20
1 E B 0 0 5 0 - 3 A
Index: 32 33 34 35 36 37 38 39 40 41 42 43 44 45 46 47
Offset 5002 (0x138a): 54 48 43 4c 53 30 34 35 31 35 52 49 30 30 31 42
T H C L S 0 4 5 1 5 R I 0 0 1 B
Index: 48 49 50 51 52 53 54 55 56 57 58 59 60 61 62 63
Offset 5018 (0x139a): 30 31 31 36 2d 30 30 31
0 1 1 6 - 0 0 1
Descriptor Text: 'ESCE IOM 1EB0050-3A THCLS04515RI001B0116-001'

## Slide 15: Built-In Support for SCSI Commands
Added Built-in Options for Several SCSI Commands:
  inquiry {page=value} Show Inquiry or specific page.
  logsense {page=value} Show Log pages supported or page.
  zerolog {page=value} Zero all Log pages or specific page.
  readcapacity16 Show disk capacity (16 byte CDB).
Support based on automation requirements (so far).
Support includes both ASCII and JSON output formats.
FYI: When page value is omitted, displays page help.

## Slide 16: Inquiry and Log Sense Pages
Additional SCSI information added for Inquiry/Log Sense
  Log Sense Protocol Specific Port page 0x18
  Pages implemented are available in both ASCII and JSON
    JSON avoids “screen scrapping”, and parses easily into Python dictionaries
    JSON includes offset/hex bytes and all reserved/obsolete fields
      This latter information can be used by automation for full verification
  Note: Others to be added, when required and requested. 

## Slide 17: Standard HGST Disk Inquiry (ASCII)
# spt dsf=/dev/sdcu inquiry logprefix=
Inquiry Information:
Peripheral Device Type: 0 (Direct Access Device)
Peripheral Qualifier: 0 (Peripheral Device Connected)
Logical Unit Conglomerate: False
Removable Media: False
ANSI Version: 6 (Complies to ANSI INCITS 513 Revision 37a)
Response Data Format: 2
Historical Support: True
Normal ACA Support: False
Additional Length: 159 (0x9f)
Supports Protection Information: True
Third Party Copy Support: False
Target Port Group Support: 0 (ALUA not supported)
Storage Controller Components: False
Multiple SCSI Ports: True
Port Receiving Inquiry: 0 (Port A)
Embedded Enclosure Services: False
Command Queuing Support: True
Vendor Identification: HGST
Product Identification: HUH728080AL4200
Firmware Revision Level: A7D8.
#

## Slide 18: Standard HGST Disk Inquiry (JSON)
# spt dsf=/dev/sdcu inquiry output-format=json
{
"Inquiry": {
"Length": 164,
"Offset": 0,
"Bytes": "00 00 06 12 9f 01 10 02 48 47 53 54 20 20 20 20 48 55 48 37 32 38 30 38 30 41 4c 34 32 30 30 20 41 37 44 38 32 45 47 31 36 34 36 4a 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 43 6f 70 79 72 69 67 68 74 20 28 43 29 20 48 47 53 54 2c 20 61 20 57 65 73 74 65 72 6e 20 44 69 67 69 74 61 6c 20 43 6f 6d 70 61 6e 79 2e 20 20 20 20 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00",
"Peripheral Device Type": 0,
"Peripheral Device Type Description": "Direct Access Device",
"Peripheral Qualifier": 0,
"Peripheral Qualifier Description": "Peripheral Device Connected",
"Reserved (byte 1, bits 0:5)": 0,
"Logical Unit Conglomerate": false,
"Removable Media": false,
"ANSI Version": 6,
"ANSI Version Description": "Complies to ANSI INCITS 513 Revision 37a",
"Response Data Format": 2,
"Historical Support": true,
"Normal ACA Support": false,
"Reserved (byte 3, bits 6:2)": 0,
"Additional Length": 159,
"Supports Protection Information": true,
"Third Party Copy Support": false,
"Target Port Group Support": 0,
"Target Port Group Support Description": "ALUA not supported",
"Obsolete (byte 5, bit 6)": 0,
"Storage Controller Components": false,
"Obsolete (byte 6, bit 0)": 0,
"Reserved (byte 6, bits 1:2)": 0,
"Obsolete (byte 6, bit 3)": 0,
"Multiple SCSI Ports": true,
"Port Receiving Inquiry": "A",
"Embedded Enclosure Services": false,
"Obsolete (byte 6, bit 7)": false,
"Vendor Specific (byte 7, bit 0)": false,
"Command Queuing Support": true,
"Reserved (byte 7, bit 2)": 0,
"Obsolete (byte 7, bits 3:3)": 0,
"Reserved (byte 7, bit 6)": 0,
"Obsolete (byte 7, bit 7)": 0,
"Vendor Identification": "HGST ",
"Product Identification": "HUH728080AL4200 ",
"JSON Status": 0
}
}
#

## Slide 19: Acquiring HGST Full Firmware Version
SG Inquiry Method
# sg_inq --page=0x03 /dev/sdl
VPD INQUIRY: ASCII information page, FRU code=0x3
Vendor specific information in hex:
00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 ................
10 00 00 00 4c 48 47 54 43 33 32 32 00 00 00 00 32 ...LHGTC322....2
20 30 30 31 43 33 32 32 30 30 30 01 33 32 32 00 31 001C322000.322.1
30 30 2f 31 39 2f 31 36 20 31 34 3a 30 35 3a 32 38 0/19/16 14:05:28
40 00 00 00 00 00 00 00 00 00 00 00 01 01 0e 24 4c ..............$L
50 48 41 34 4b 00 00 00 45 4e 43 5f 30 36 47 5f 52 HA4K...ENC_06G_R
60 45 4c 45 41 53 45 00 62 6c 64 63 72 65 77 00 00 ELEASE.bldcrew..
70 00 00 00 66 6f 72 67 65 30 32 00 00 00 00 00 00 ...forge02......
80 00 00 00 43 3a 2f 54 65 6d 70 2f 63 63 62 37 2f ...C:/Temp/ccb7/
90 52 33 32 32 2f 6c 69 62 72 61 72 79 2f 4c 48 41 R322/library/LHA
a0 34 4b 00 00 00 00 05 00 01 00 00 00 00 00 00 00 4K..............
b0 00 00 00 00 00 00 02 43 33 32 32 .......C322
#
Python Snippet: (old way)
message = "Find full firmware version for SAS drive"
command = "sudo {0}/sg_inq -p0x03 -H {1} | grep 10 | head -1 | awk -F '.' '{{print $NF}}'".format(self._tools_directory, drive)
sg_inq_output = self._run_command(command=command, message=message, logger=logger, shell=True)
firmware = sg_inq_output.strip()
Versus SPT JSON Method
# spt dsf=/dev/sdl inquiry page=0x03 ofmt=json
{
"ASCII Information": {
"Length": 192,
"Page Code": "0x03",
"Page Length": 188,
"Bytes": "00 03 00 bc 00 00 00 ...”
…
"ASCII uCode Identifier": "LHGTC322",
"ASCII Servo Part Number": "2001",
…
"Code Mode Description": "OM_DISK - Drive is running code loaded from disk",
"Flash Code Major Version": "C3",
"Flash Code Minor Version": "22",
"JSON Status": 0
}
}
Python Snippet: (new way)
message = "Find full firmware version for SAS drive"
command = "{0}/spt dsf={1} inquiry page=ascii_info_page03 output-format=json emit=".format(self._tools_directory, disk_dev)
spt_json = self._run_command(command=command, message=message, logger=logger, shell=False)
page03 = json.loads(spt_json)
current_firmware = page03['ASCII Information']['ASCII uCode Identifier'].strip()

## Slide 20: Showing SCSI Log Sense Page Code/Names
# spt logprefix= logsense page= (pages in green support decode functions)
Log Page Codes/Names:
0x00 - Supported (supported)
0x01 - Buffer Overrun/Underrun Counter (overrun_underrun)
0x02 - Write Error Counter (write_error)
0x03 - Read Error Counter (read_error)
0x04 - Read Reverse Error Counter (read_reverse)
0x05 - Verify Error Counter (verify_error)
0x06 - Non-medium error counter (non-medium)
0x07 - Last n error events (last_error_events)
0x08 - Format Status (format_status)
0x0b - Last n Deferred or Async Events (last_deferred_events)
0x0a - Sequential-Access Device (sequential_access)
0x0c - Logical Block Provisioning (logical_block_provisioning)
0x0d - Temperature (temperature)
0x0e - Start-stop Cycle Counter (start_stop_cycle)
0x0f - Application Client (application_client)
0x10 - Self-Test Results (self_test_results)
0x11 - Solid State Media (solid_state_media)
0x15 - Background-Scan Results (background_scan)
0x17 - Non-Volatile Cache (non_volatile_cache)
0x18 - Protocol Specific Port (protocol_specific_port)
0x19 - Statistics and Performance (statistics_performance)
0x1a - SMART Status & Temp Reading (smart_status)
0x2f - Informational Exceptions (informational)
0x30 - Performance Counters (performance)
0x37 - Miscellaneous Data Counters (misc_data)
#

## Slide 21: Log Sense Protocol Specific Page
# spt dsf=/dev/sddf logsense page=protocol_specific_port logprefix=
Protocol Specific Port Parameters (Page 0x18 - Current Cumulative Values):
Page Code: 0x18
Subpage Code: 0
Page Length: 216 (0xd8)
Parameter Code: 0x1 (Primary Port)
Format and Linking: 3 (Binary format list)
Target Save Disable (TSD): 0
Parameter Length: 104 (0x68)
Protocol Identifier: 0x6 (SAS Serial SCSI Protocol)
Generation Code: 1
Number of PHYs: 1
SAS Phy Log Descriptor: 0
Phy Identifier: 0
SAS Phy Log Descriptor Length: 96 (0x60)
Attached Reason: 8 (Phy Test Function Stopped)
Attached Device Type: 2 (Expander device)
Negotiated Physical Link Rate: 0xa (6 Gbps)
Last Link Reset Reason: 0 (Power On)
SMP Initiator Port: True
STP Initiator Port: False
SSP Initiator Port: False
SMP Target Port: True
STP Target Port: False
SSP Target Port: False
The SAS Address: 0x5000cca2510349b5
Attached SAS Address: 0x5000ccab00ff010b
Attached Phy Identifier: 13
Invalid Dword Count: 0
Running Disparity Error Count: 0
Loss of Dword Synchronization: 0
Phy Reset Problem: 0
Phy Event Descriptor Length: 12 (0xc)
Number of Event Descriptors: 4
…

## Slide 22: SCSI Read Capacity (16) Example
# spt dsf=/dev/sddf logprefix= readcapacity16
Read Capacity(16) Data: (data length 32 bytes)
Maximum Capacity: 2441609216 (9537536.000 megabytes)
Block Length: 4096
Protection Enabled: No
Protection Type: 0
Logical Blocks per Physical Exponent: 0 (1 blocks per physical)
Protection Information Exponent: 0
Logical Block Provisioning Management: No (Full Provisioned)
Logical Block Provisioning Read Zeroes: No
Lowest Aligned Logical Block Address: 0
# spt dsf=/dev/sddf logprefix= readcapacity16 output-format=json
{
"Read Capacity(16)": {
"Length": 32,
"Offset": 0,
"Bytes": "00 00 00 00 91 87 ff ff 00 00 10 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00",
"Maximum Capacity": 2441609216,
"Block Length": 4096,
"Protection Enabled": false,
"Protection Type": 0,
"Logical Blocks per Physical Exponent": 0,
"Protection Information Exponent": 0,
"Logical Block Provisioning Management": false,
"Logical Block Provisioning Read Zeroes": false,
"Lowest Aligned Logical Block Address": 0,
"JSON Status": 0
}
}
#

## Slide 23: Showing SCSI Operation Codes
$ spt showopcodes
Opcode Subcode Direction Encode Decode Default Opcode Name
------ ------- --------- ------ ------ --------- -----------
0x40 0x00 none no no 0 Change Definition
0x39 0x00 none no no 0 Compare
0x18 0x00 none no no 0 Copy
0x3a 0x00 none no no 0 Copy and Verify
0x46 0x00 none no no 0 Get Configuration
0x12 0xff read yes yes 0 Inquiry
0x12 0x00 none no no 0 Inquiry - Supported Pages
0x12 0x80 none no no 0 Inquiry - Serial Number
0x12 0x83 none no no 0 Inquiry - Device Identification
0x12 0x85 none no no 0 Inquiry - Management Network Addresses
0x12 0x86 none no no 0 Inquiry - Extended Inquiry Data
0x12 0x87 none no no 0 Inquiry - Mode Page Policy
0x12 0x8f none no no 0 Inquiry - Third-party Copy
0x12 0xb0 none no no 0 Inquiry - Block Limits
0x12 0xb2 none no no 0 Inquiry - Logical Block Provisioning
0x4c 0x00 write yes no 0 Log Select
0x4d 0x00 read yes yes 0 Log Sense
0x15 0x00 none no no 0 Mode Select(6)
0x55 0x00 none no no 0 Mode Select(10)
0x1a 0x00 none no no 0 Mode Sense(6)
0x5a 0x00 none no no 0 Mode Sense(10)
0x3c 0x00 none no no 0 Read Buffer
0x1c 0x00 read yes yes 0 Receive Diagnostic
0x03 0x00 none no no 0 Request Sense
0x1d 0x00 write yes yes 0 Send Diagnostic
0x00 0x00 none no no 0 Test Unit Ready
…
0x8a 0x00 write yes no 0 Write(16)
0x8e 0x00 write yes no 0 Write and Verify(16)
0x8f 0x00 none yes no 65536 Verify(16)
0x91 0x00 none no no 0 Synchronize Cache(16)
0x93 0x00 write yes no 65536 Write Same(16)
0x9e 0x00 read no no 0 Service Action In(16)
0x9e 0x10 read yes yes 0 Read Capacity(16)
0x9e 0x12 none no no 0 Get LBA Status(16)
0x89 0x00 none no no 0 Compare and Write(16)

## Slide 24: Concurrent Testing of Multiple Devices
Multiple Jobs via Script File (same as dt, but no job control)
# cat dospt-tur.sh
#!/bin/bash
disks=${disks:-""}
if [[ -z $disks ]];
then
disks=$(lsscsi | fgrep disk | awk '{print $NF}')
if [[ -z ${disks} ]]; then
echo "Warning: No disks were found!"
exit 1
fi
fi
rm -f spt-tur.spt
for disk in ${disks}
do
echo "dsf=${disk} cdb=0 status=good retry=100 msleep=100 enable=wait enable=async" >> spt-tur.spt
done
echo "sleep=3s" >> spt-tur.spt
spt script=spt-tur
exit $?
# ./dospt-tur.sh
# echo $?
0
#

## Slide 25: Test Check Options
Automatically Verify SCSI Status Information
  Test Check Options:
  resid=value The expected residual.
  transfer=value The expected transfer count.
  status=value The expected SCSI status.
  skey=value The expected SCSI sense key.
  asc=value The expected SCSI sense code.
  asq=value The expected SCSI sense qualifier.
  Note: The enable=wait option can be used to wait for status.
  SCSI Status Keyword Value
  ----------- ------- -----
  GOOD good 0x00
  CHECK_CONDITION cc 0x02
  CONDITION_MET cmet 0x04
  BUSY busy 0x08
  INTERMEDIATE inter 0x10
  INTER_COND_MET icmet 0x14
  RESERVATION_CONFLICT rescon 0x18
  COMMAND_TERMINATED term 0x22
  QUEUE_FULL qfull 0x28
  ACA_ACTIVE aca_active 0x30
  TASK_ABORTED aborted 0x40
  Example:
  # spt cdb=0 status=good retry=100 msleep=100 enable=wait

## Slide 26: Test Check Example
# lsscsi --generic | fgrep sdl
[0:0:11:0] disk HGST HUH721010AL4204 C322 /dev/sdl /dev/sg11
# spt dsf=/dev/sg11 op=lun_reset ; spt dsf=/dev/sg11 cdb=0 status=cc skey=6 asc=0x29 asq=0x3
# spt dsf=/dev/sg11 op=lun_reset ; spt dsf=/dev/sg11 cdb=0 status=good logprefix=
Result for Test Unit Ready
Expected:
SCSI Status: 00h = SCSI_GOOD
Sense Key: 00h = NO SENSE
asc/ascq: 00h/00h = No additional sense information
Actual:
SCSI Status: 02h = SCSI_CHECK_CONDITION
Sense Key: 06h = UNIT ATTENTION
asc/ascq: 29h/03h = Bus device reset function occurred
ERROR: Error number 1 occurred on Tue Oct 10 10:24:11 2017
ERROR: Unexpected response for SCSI opcode 0x0 (Test Unit Ready)
# echo $?
255
#

## Slide 27: Expect Options
Options to Automatically Verify Data Received
  Expect Data Options:
  exp_radix={any,dec,hex} The default is any radix.
  exp[ect]=type:byte_index:{string|value},...
  Where type is:
  C[HAR] Character strings to expect.
  B[YTE] Byte (8 bit) values to expect.
  S[SHORT] Short (16 bit) values to expect.
  W[ORD] Word (32 bit) values to expect.
  L[ONG] Long (64 bit) values to expect.
  Note: Byte index and values are taken as decimal (by default).
  Example Inquiry Verify:
  # spt dsf=/dev/sg42 \
  cdb='12 00 00 00 ff 00' dir=read length=255 \
  expect=BYTE:0:0x0d,0x00,0x06,0x02,0x5b,0x00,0x40,0x02 \
  expect=C:8:'HGST ','STOR ENCL JBOD ' \
  expect=CHAR:32:'0116‘ disable=verbose
  Please see Test Check Options for more test controls.

## Slide 28: Expect Error Reporting
Changed “HGST” to “WDC “ to generate this error:
# spt dsf=/dev/sg42 \
inquiry expect=BYTE:0:0x0d,0x00,0x06,0x02,0x5b,0x00,0x40,0x02 \
expect=C:8:'WDC ','STOR ENCL JBOD ' expect=CHAR:32:'0116' \
disable=decode,verbose
spt (j:1 t:1): ERROR: Error number 1 occurred on Wed Oct 11 21:18:14 2017
spt (j:1 t:1): Failure while verifying Inquiry data on device /dev/sg42 (thread 1)
-> Offset 000008: Expected Data: 87 (0x57, 'W') Received Data: 72 (0x48, 'H')
-> Offset 000009: Expected Data: 68 (0x44, 'D') Received Data: 71 (0x47, 'G')
-> Offset 000010: Expected Data: 67 (0x43, 'C') Received Data: 83 (0x53, 'S')
-> Offset 000011: Expected Data: 32 (0x20, ' ') Received Data: 84 (0x54, 'T')
spt (j:1 t:1): Data Bytes: 96, Expect Entries: 36, Correct Entries: 32, Incorrect Entries: 4
# echo $?
255
#

## Slide 29: Example SPT Script for SES Page Verification
#
# spt Script to verify MP SES Configuration Page 1.
#
$SPT_DEVICE=${SPT_DEVICE:?"Please define SPT_DEVICE for the /dev/sgNN device!}
enable=scriptverify
exp_radix=hex
$VENDOR=${VENDOR:-'WDC '}
$PRODUCT=${PRODUCT:-'InfiniFlash P200'}
$REVISION=${REVISION:-'0001'}
...
#
# SES Configuration Page 1:
#
rcvdiag page=configuration disable=decode,verbose transfer=248 \
#
# 00000 (0x0000) 01 00 00 f4 00 00 00 00
# Page Code: 0x1
# Number of Secondary Enclosures: 0
# Page Length: 244
# Generation Number: 0
#
expect=BYTE:0:01,00,00,f4,00,00,00,00 \
#
# 00008 (0x0008) 11 00 0a 24 50 00 cc ab 05 01 01 80 57 44 43 20
# 00024 (0x0018) 20 20 20 20 49 6e 66 69 6e 69 46 6c 61 73 68 20
# 00040 (0x0028) 50 32 30 30 30 30 30 31
# Enclosure Descriptor List:
# Number Enclosure Services Processes: 1
# Relative Enclosure Services Process ID: 1
# Subenclosure Identifier: 0 (Primary)
# Number of Type Descriptor Headers: 10
# Enclosure Descriptor Length: 36
# Enclosure Logical Identifier: 0x5000ccab05010180
# Vendor Identification: WDC
# Product Identification: InfiniFlash P200
# Product Revision Level: 0001
#
expect=BYTE:8:11,00,0a,24,50,00,cc,ab,05,01,01,80 \
expect=CHAR:14:"${VENDOR}","${PRODUCT}","${REVISION}" \
...

## Slide 30: Unpack SCSI Data Options
A Format String to Unpack Various Data Received:
Unpack Data Options:
unpack=string The unpack format string.
unpack_fmt={dec,hex} The unpack data format. (Default: dec)
Where unpack format string is:
C[HAR]:[index]:length Character of length.
F[IELD]:[index]:[start]:length Extract bit field.
O[FFSET]:index Set the buffer offset.
B[YTE][:index] Decode byte (8 bit) value.
S[HORT][:index] Decode short (16 bit) value.
W[ORD][:index] Decode word (32 bit) values.
L[ONG][:index] Decode long (64 bit) values.
Inquiry Unpack Examples:
# spt dsf=/dev/sdb inquiry disable=decode \
unpack='Device Type: %BYTE, Vendor: %CHAR:8:8, Product: %C::16, Revision: %C::4\n'
OR Create your own JSON: (multiple unpack's permitted)
# spt dsf=/dev/sdb inquiry disable=decode \
unpack='{ "Device Type": %BYTE, "Vendor": "%C:8:8",' \
unpack=' "Product": "%C::16", "Revision": "%C::4" }\n'

## Slide 31: Emit Status Control Strings
SPT does NOT display statistics automatically.
Roll-Your-Own Status/Statistics via: (or use emit=default)
  # export SPT_EMIT_STATUS="
  Thread: %thread
  Device Name: %dsf
  SCSI Name: %scsi_name
  SCSI CDB: %cdb
  Iterations: %iterations
  Exit Status: %status = %status_msg
  Host Status: %host_status = %host_msg
  Driver Status: %driver_status = %driver_msg
  SCSI Status: %scsi_status = %scsi_msg
  Sense Code: %sense_code = %sense_msg
  Sense Key: %sense_key = %skey_msg
  asc/asq: (%asc, %asq) = %ascq_msg
  Transferred: %xfer (data bytes transferred)
  Residual: %resid (bytes not transferred)
  Total Blocks: %total_blocks
  Total Xferred: %total_xfer bytes
  Sense Data: %sense_data\n“
See “spt help” for full list of Emit Status Control strings.

## Slide 32: Example Emit Status Output
# spt dsf=/dev/sdl cdb=0x8e starting=0 bs=64k limit=1g emit=default (Note: Writes all zero’s, by default)
spt (j:1 t:1):
spt (j:1 t:1): Thread: 1
spt (j:1 t:1): Device Name: /dev/sdl
spt (j:1 t:1): Device Info: Block Length=4096, Capacity=2441609216
spt (j:1 t:1): Block Range: 0 - 262144
spt (j:1 t:1): SCSI Name: Write and Verify(16)
spt (j:1 t:1): SCSI CDB: 8e 00 00 00 00 00 00 03 ff 80 00 00 00 80 00 00
spt (j:1 t:1): Data Direction: write
spt (j:1 t:1): Data Length: 524288
spt (j:1 t:1): Exit Status: 0 = SUCCESS
spt (j:1 t:1): Host Status: 0 = DID_OK
spt (j:1 t:1): Driver Status: 0 = DRIVER_OK
spt (j:1 t:1): SCSI Status: 0 = SCSI_GOOD
spt (j:1 t:1): Sense Code: 0 = NO CODE
spt (j:1 t:1): Sense Key: 0 = NO SENSE
spt (j:1 t:1): asc/asq: (00, 00) = No additional sense information
spt (j:1 t:1): Bytes Transferred: 524288 (data bytes transferred)
spt (j:1 t:1): Residual: 0 (bytes not transferred)
spt (j:1 t:1): Iterations: 1
spt (j:1 t:1): Total Bytes: 1073741824
spt (j:1 t:1): Total Blocks: 262144
spt (j:1 t:1): Total Operations: 2049
spt (j:1 t:1): Sense Data: 00 00 00 00 00 00 00 00
spt (j:1 t:1): Elapsed Time: 00m38.53s
spt (j:1 t:1): Starting Time: Thu Oct 12 12:32:00 2017
spt (j:1 t:1): Ending Time: Thu Oct 12 12:32:39 2017
spt (j:1 t:1):
#

## Slide 33: Triage/Recovery Support
Display of Full Sense Data via enable=sense
  for xcopy, both copies of sense data displayed
Automatic Recovery via enable=recovery
  Error Conditions Retried:
    Unit Attention, SCSI Busy, and Queue Full
    Not Ready, in the process of becoming ready
    Linux specific MPIO workaround
      a read request is required to force path failover!
Error Recovery Options:
  recovery_delay=value - The amount of time to delay before retrying. (Default: 2 secs)
  recovery_retries=value - The number of times to retry a SCSI request. (Default: 60)

## Slide 34: Support for I/O Ranges
I/O Ranges Automatically:
  Sets the I/O direction
  Adds enable=encode,decode (as required)
  Automatically fills in the CDB fields
  Optionally compares data read
Support for I/O ranges for these CDB’s
  Read/Write (6, 10, and 16 byte)
  Verify and Write Same (10 and 16 byte)
  Unmap (frees blocks)
Examples:
  # export SPT_DEVICE=/dev/sdl
  # SCSI_OPCODE_READ_16=0x88
  # SCSI_OPCODE_WRITE_16=0x8a
  # SCSI_OPCODE_WRITE_SAME_16=0x93
  # spt cdb=${SCSI_OPCODE_WRITE_16} bs=32k starting=0 ptype=iot enable=sense
  # spt cdb=${SCSI_OPCODE_READ_16} bs=32k starting=0 ptype=iot enable=compare
  # spt cdb=${SCSI_OPCODE_WRITE_SAME_16} starting=0 blocks=16k enable=sense

## Slide 35: Support for I/O Modes
Similar to DT’s I/O Modes
I/O Mode Support:
  iomode=mode - Set I/O mode to: {copy, mirror, test, or verify}
  copy/verify added for copying and verifying LUNs
  mirror mode added to verify synchronous mirrors
    writing to one LUN should be mirrored to another LUN
Examples:
  # spt dsf=${SRC_DEVICE} dsf1=${DST_DEVICE} length=32k iomode=copy enable=compare
  # spt dsf=${SRC_DEVICE} dsf1=${DST_DEVICE} length=32k iomode=verify
  # spt dsf=${DST_DEVICE} dsf1=${DST_DEVICE} length=32k \
  writetype=writev16 iomode=mirror ptype=iot slices=10

## Slide 36: Support for Multiple Slices
Slices Create Multiple I/O Ranges
Each Slice is a Thread with its’ Own Range:
  # SCSI_VERIFY_16=0x8f
  # spt cdb=${SCSI_VERIFY_16} starting=0 slices=3 limit=1g \
  enable=Debug,sense,recovery logprefix=
  Device: /dev/sdl, Device Size: 4096 bytes, Capacity: 2441609216 blocks (thread 0)
  Device: /dev/sdl, Starting lba=0, ending lba=262143, block limit=262144 (thread 0)
  Device: /dev/sdl, Starting lba=0, ending lba=87380, block limit=87381 (thread 1)
  Device: /dev/sdl, Starting lba=87381, ending lba=174761, block limit=87381 (thread 2)
  Device: /dev/sdl, Starting lba=174762, ending lba=262143, block limit=87382 (thread 3)
  #
Create lots of Slices to Generate Higher Load!

## Slide 37: Support for Disruptive Testing
Several popular methods include:
  Setting incorrect CDB fields.
  Sending unsupported CDB opcodes.
  Sending incorrect I/O direction or length.
  Sending high I/O to test Queue Full conditions.
  Setting short timeouts to verify abort sequences.
    On Linux, must use /dev/sgXX for short timeouts
    Requests via /dev/sdXX (block device) enforce a minimum timeout:
      linux/blkdev.h: #define BLK_MIN_SG_TIMEOUT (7 * HZ) (7 seconds)
  Sending Task Management Functions (TMF):
    Bus Reset (may be simulated based on protocol)
    LUN Reset
    Target Reset

## Slide 38: Example of Forcing Command Timeouts
# lsscsi -g | fgrep sdl
[0:0:11:0] disk HGST HUH721010AL4204 C322 /dev/sdl /dev/sg11
# spt dsf=/dev/sg11 cdb=${SCSI_VERIFY_16} starting=0 blocks=0xffff limit=1g timeout=1 logprefix=
ERROR: Error number 1 occurred on Wed Oct 11 16:21:14 2017
Verify(16) failed on device /dev/sg11 (thread 1)
SCSI CDB: 8f 00 00 00 00 00 00 00 00 00 00 00 ff ff 00 00, dir=none, length=0
SCSI Status = 0 (SCSI_GOOD)
Host Status = 0x3 (DID_TIME_OUT), Driver Status = 0 (DRIVER_OK)
Sense Key = 0 = NO SENSE, Sense Code/Qualifier = (0, 0) - No additional sense information
# dmesg --ctime | tail
…
[Wed Oct 11 16:17:32 2017] sd 0:0:11:0: attempting task abort! scmd(ffff881030c3b380)
[Wed Oct 11 16:17:32 2017] sd 0:0:11:0: [sg11] tag#0 CDB: Verify(16) 8f 00 00 00 00 00 00 00 00 00 00 00 ff ff 00 00
[Wed Oct 11 16:17:32 2017] scsi target0:0:11: handle(0x0015), sas_address(0x5000cca2510285c9), phy(11)
[Wed Oct 11 16:17:32 2017] scsi target0:0:11: enclosure_logical_id(0x5001636001caa0bd), slot(11)
[Wed Oct 11 16:17:32 2017] scsi target0:0:11: enclosure level(0x0000),connector name( )
[Wed Oct 11 16:17:32 2017] sd 0:0:11:0: task abort: SUCCESS scmd(ffff881030c3b380)
#

## Slide 39: Extended SCSI CDB Support
SCSI CDB’s Extended by encode/decode
I/O Options Enable this Automatically
Read Capacity(16) Example:
  # spt cdb='9e 10' dir=read length=32 enable=encode,decode disable=verbose
  Read Capacity(16) Data: (data length 32 bytes)
  Maximum Capacity: 204800 (100.000 megabytes)
  Block Length: 512
  Protection Enabled: No
  Protection Type: 0
  Logical Blocks per Physical Exponent: 3
  Protection Information Exponent: 0
  Thin Provisioning Enabled (LBPME): Yes
  Thin Provisioning Read Zeroes (LBPRZ): Yes
  Lowest Aligned Logical Block Address: 0
  #

## Slide 40: Extended SCSI CDB Support (continued…)
SCSI Inquiry Low Level Equivalence:
  inquiry = ‘cdb='12 00 00 00 ff 00' dir=read length=255 enable=encode,decode disable=verbose
  # spt inquiry logprefix=
  Inquiry Information:
  Peripheral Device Type: 0xd (Enclosure Services Device)
  Peripheral Qualifier: 0 (Peripheral Device Connected)
  Logical Unit Conglomerate: False
  Removable Media: False
  ANSI Version: 6 (Complies to ANSI INCITS 513 Revision 37a)
  Response Data Format: 2
  Historical Support: False
  Normal ACA Support: False
  Additional Length: 91 (0x5b)
  Supports Protection Information: False
  Third Party Copy Support: False
  Target Port Group Support: 0 (ALUA not supported)
  Storage Controller Components: False
  Multiple SCSI Ports: False
  Embedded Enclosure Services: True
  Command Queuing Support: True
  Vendor Identification: HGST
  Product Identification: STOR ENCL JBOD
  Firmware Revision Level: EL14
  Detailed Firmware Revision: -004 04.08.01
  Version Descriptor SAM-5: 0xa0
  Version Descriptor SAS-2: 0xc20
  Version Descriptor SPC-4: 0x460
  Version Descriptor SES-3: 0x580
  #

## Slide 41: Enhanced Script File Support
SPT Supports Script Files (5 levels deep)
Environment Variables Now Expanded or Set:
  # Enabling Debug shows us each spt command being executed.
  enable=Debug
  $SCSI_OPCODE_READ_16=0x88
  $SCSI_OPCODE_WRITE_16=0x8a
  $SCSI_OPCODE_WRITE_AND_VERIFY_16=0x8e
  $SCSI_OPCODE_WRITE_SAME_16=0x93
  $SLICES=3
  $IO_LENGTH=64k
  $ENABLE_OPTIONS="enable=Debug,sense"
  $READ_OPTIONS="cdb=${SCSI_OPCODE_READ_16} dir=read length=${IO_LENGTH} ${ENABLE_OPTIONS}"
  $WRITE_OPTIONS="cdb=${SCSI_OPCODE_WRITE_16} dir=write length=${IO_LENGTH} ${ENABLE_OPTIONS}"
  $WRITE_SAME_OPTIONS="cdb=${SCSI_OPCODE_WRITE_SAME_16} starting=0 blocks=0xffff ${ENABLE_OPTIONS}"
  # Initialize the source LUN with the IOT pattern.
  dsf=${SRC_DEVICE} ${WRITE_OPTIONS} starting=0 ptype=iot slices=${SLICES}
  # Zero the destination LUN using Write Same.
  dsf=${DST_DEVICE} ${WRITE_SAME_OPTIONS}
  # Copy from one LUN to another with data verification.
  dsf=${SRC_DEVICE} dsf1=${DST_DEVICE} length=${IO_LENGTH} iomode=copy enable=compare,image emit=multi slices=10
  …

## Slide 42: SPT Roadmap
Add more Inquiry, Log, and Mode pages.
Add firmware download and Format support.
Add JSON output format for other SCSI operations.
Add SCSI compliance verification.
Add support for Linux “bsg” SCSI interface.
Add support for multiple devices. (like dt)
Job Control for waiting on Async Threads. (like dt)
Add server/client message passing using ZeroMQ.
Note: Not likely to be done now that I’m retired! 