## Slide 1: SCSI Pass-Through (SPT) 2019 Update (TOI) by Robin T. Miller Robin.Miller@hpe.com
Updated: September 23rd, 2025

## Slide 2: Agenda
What is SPT?
Why use SPT?
SPT Features
New Features
SPT Roadmap

## Slide 3: SCSI Pass-Through (SPT) Utility
SPT allows SCSI testing via the SCSI pass-through API
  This is an OS specific user level API for issuing SCSI operations.
Supported on most OS’s, except OSX (lacks SCSI API)
A fair amount of code originated from DT tool
SPT is open source, and is available on GitHub:
  https://github.com/RobinTMiller/spt
    Note: Github does NOT include Vendor Unique (VU) extensions.
Storage Enclosure Services (SES) support

## Slide 4: Why Use This SPT Tool?
Advanced Testing Requires Advanced Test Tools
Key SPT Features: (one tool versus many)
  Specifically designed for SCSI testing
  Supports multiple jobs/threads for high load & stress
  Supports JavaScript Object Notation (JSON)
Useful for developers, automation, and support.
This TOI will hopefully whet your appetite!
We have internal developer (Robin) and support! 

## Slide 5: SPT Features
Send/Receive Diagnostic Support (added for SES pages)
Support for I/O Ranges (for read/write/verify operations)
Support for I/O Modes (copy/verify/mirror operations)
Support for Multiple Slices (threads for higher load & stress)
Support for Extended Copy Operations (two methods).
Triage/Recovery Support (detailed errors, recovery, etc)
Extended SCSI CDB Support (encode/decode CDB’s)
Enhanced Script File Support (custom test scripts)
Emit Status Control Strings (roll your own output format)
Test Check / Expect Options (automatic data/sense checks)
Provides ASCII and JSON output formats! (work-in-progress)
Support to unpack SCSI data (decode data in user format)

## Slide 6: New SPT Version 3.x Features
SES LED Control
Log Pages: counters, temperature
Built-in Request Sense parsing, and others
Show Devices Formats:
  Summary Format
  Long Format
  Roll-Your-Own
  JSON Format
List Disks/Enclosures Script: lsdisks (Python spt wrapper)
Test Commands: selftest, extended self test, etc
Python Shared Library via CTYPES API

## Slide 7: SCSI XCOPY Acronyms
Extended Copy (XCOPY) (older method used by Vmware)
Token Based XCOPY:
  Newer method used by Windows, aka ODX
  Populate Token (PT)
  Receive ROD Token Information (RTTI)
    ROD = Representation of Data
  Write Using Token (WUT)
  Token - A Token represents point-in-time copy of LBA ranges from source LUN

## Slide 8: What Are (some of) The Differences?
Non-Token Based XCOPY: (VMware)
  One SCSI Command:
    Extended Copy CDB (XCOPY)
  Inquiry VPD Device ID Identifier required
  Multiple Sources, One Destination LUN
Token Based XCOPY: (Microsoft)
  Multiple SCSI Commands:
    PT / RTTI / WUT / RTTI
  One Source and One Destination LUN
  Token XCOPY Volume Requirements

## Slide 9: SCSI Pass-Through (SPT) Support
Supports Both XCOPY Formats:
  cdb=0x83 initiates non-token xcopy
  cdb='0x83 0x11‘ initiates token xcopy
Multiple Sources for non-token xcopy
Multiple Destination for token xcopy
Zero ROD Supported for Token xcopy
  same as unmapping blocks via Unmap CDB
Extended Debug (enable=xdebug)
  automatically dumped during errors

## Slide 10: Preparing Disks for Extended Copy Testing
# spt dsf=/dev/mapper/mpatha cdb=8e bs=32k starting=0 pattern=iot slices=10 enable=Debug
spt (j:0 t:0): Device: /dev/mapper/mpatha, Device Size: 512 bytes, Capacity: 20971520 blocks (thread 0)
spt (j:0 t:0): Device: /dev/mapper/mpatha, Starting lba=0, ending lba=20971519, block limit=20971520 (thread 0)
spt (j:1 t:2): Device: /dev/mapper/mpatha, Starting lba=2097152, ending lba=4194303, block limit=2097152 (thread 2)
spt (j:1 t:1): Device: /dev/mapper/mpatha, Starting lba=0, ending lba=2097151, block limit=2097152 (thread 1)
spt (j:1 t:3): Device: /dev/mapper/mpatha, Starting lba=4194304, ending lba=6291455, block limit=2097152 (thread 3)
spt (j:1 t:4): Device: /dev/mapper/mpatha, Starting lba=6291456, ending lba=8388607, block limit=2097152 (thread 4)
spt (j:1 t:8): Device: /dev/mapper/mpatha, Starting lba=14680064, ending lba=16777215, block limit=2097152 (thread 8)
spt (j:1 t:6): Device: /dev/mapper/mpatha, Starting lba=10485760, ending lba=12582911, block limit=2097152 (thread 6)
spt (j:1 t:5): Device: /dev/mapper/mpatha, Starting lba=8388608, ending lba=10485759, block limit=2097152 (thread 5)
spt (j:1 t:7): Device: /dev/mapper/mpatha, Starting lba=12582912, ending lba=14680063, block limit=2097152 (thread 7)
spt (j:1 t:9): Device: /dev/mapper/mpatha, Starting lba=16777216, ending lba=18874367, block limit=2097152 (thread 9)
spt (j:1 t:10): Device: /dev/mapper/mpatha, Starting lba=18874368, ending lba=20971519, block limit=2097152 (thread 10)
# spt dsf=/dev/mapper/mpatha cdb='9e 12' starting=0 logprefix=
Get LBA Status Information:
Mapped Blocks: 20971520
Deallocated Blocks: 0
Total Blocks: 20971520
# spt dsf=/dev/mapper/mpathb cdb='42' starting=0 logprefix=
# spt dsf=/dev/mapper/mpathb cdb='9e 12' starting=0 logprefix=
Get LBA Status Information:
Mapped Blocks: 0
Deallocated Blocks: 20971520
Total Blocks: 20971520
#

## Slide 11: Non-Token Based XCOPY
# spt cdb=0x83 enable=recovery,sense src=/dev/mapper/mpatha dst=/dev/mapper/mpathb emit=multi logprefix=
Thread: 1
Source Device: /dev/mapper/mpatha
Source Info: Block Length=512, Capacity=20971520
Block Range: 0 - 20971520
Destination Device: /dev/mapper/mpathb
Destination Info: Block Length=512, Capacity=20971520
Block Range: 0 - 20971520
SCSI Name: Extended Copy
SCSI CDB: 83 00 00 00 00 00 00 00 00 00 00 00 00 6c 00 00
Data Direction: write
Data Length: 512
Exit Status: 0 = SUCCESS
Host Status: 0 = DID_OK
Driver Status: 0 = DRIVER_OK
SCSI Status: 0 = SCSI_GOOD
Sense Code: 0 = NO CODE
Sense Key: 0 = NO SENSE
asc/asq: (00, 00) = No additional sense information
Bytes Transferred: 108 (data bytes transferred)
Residual: 0 (bytes not transferred)
Iterations: 1
Total Bytes: 276480
Total Blocks: 20971520
Total Operations: 2564
Sense Data: 00 00 00 00 00 00 00 00
Elapsed Time: 00m12.90s
Starting Time: Fri Feb 1 14:27:50 2019
Ending Time: Fri Feb 1 14:28:03 2019
#

## Slide 12: Token Based XCOPY Example
# spt cdb='0x83 0x11' enable=recovery,sense src=/dev/mapper/mpatha dst=/dev/mapper/mpathb emit=multi logprefix=
Thread: 1
Source Device: /dev/mapper/mpatha
Source Info: Block Length=512, Capacity=20971520
Block Range: 0 - 20971520
Destination Device: /dev/mapper/mpathb
Destination Info: Block Length=512, Capacity=20971520
Block Range: 0 - 20971520
SCSI Name: XCOPY - Write Using Token
SCSI CDB: 83 11 00 00 00 00 01 8b 46 06 00 00 02 28 00 00
Data Direction: write
Data Length: 512
Exit Status: 0 = SUCCESS
Host Status: 0 = DID_OK
Driver Status: 0 = DRIVER_OK
SCSI Status: 0 = SCSI_GOOD
Sense Code: 0 = NO CODE
Sense Key: 0 = NO SENSE
asc/asq: (00, 00) = No additional sense information
Bytes Transferred: 32 (data bytes transferred)
Residual: 773 (bytes not transferred)
Iterations: 1
Total Bytes: 88320
Total Blocks: 20971520
Total Operations: 644
Sense Data: 00 00 00 00 00 00 00 00
Elapsed Time: 00m10.60s
Starting Time: Fri Feb 1 14:29:50 2019
Ending Time: Fri Feb 1 14:30:01 2019
#

## Slide 13: Verifying the XCOPY Operation
# spt iomode=verify length=32k dsf=${SRC} starting=0 dsf1=${DST} starting=0 emit=multi enable=compare,recovery,sense logprefix=
Thread: 1
Source Device: /dev/mapper/mpathb
Source Info: Block Length=512, Capacity=20971520
Block Range: 0 - 20971520
Destination Device: /dev/mapper/mpatha
Destination Info: Block Length=512, Capacity=20971520
Block Range: 0 - 20971520
SCSI Name: Read(16)
SCSI CDB: 88 00 00 00 00 00 01 3f ff c0 00 00 00 40 00 00
Data Direction: read
Data Length: 32768
Exit Status: 0 = SUCCESS
Host Status: 0 = DID_OK
Driver Status: 0 = DRIVER_OK
SCSI Status: 0 = SCSI_GOOD
Sense Code: 0 = NO CODE
Sense Key: 0 = NO SENSE
asc/asq: (00, 00) = No additional sense information
Bytes Transferred: 32768 (data bytes transferred)
Residual: 0 (bytes not transferred)
Iterations: 1
Total Bytes: 21474836480
Total Blocks: 41943040
Total Operations: 655362
Sense Data: 00 00 00 00 00 00 00 00
Elapsed Time: 01m35.04s
Starting Time: Fri Feb 1 14:13:29 2019
Ending Time: Fri Feb 1 14:15:04 2019
#

## Slide 14: Alternate Data Verification with dt Tool
# dt src=${SRC} dst=${DST} iomode=verify bs=32k slices=10 workload=job_stats_only logprefix= disable=scsi
Operating System Information:
Host name: rtpqa-rhel001 (10.64.21.59)
User name: romiller
Process ID: 28933
OS information: Linux 3.10.0-514.el7.x86_64 #1 SMP Wed Oct 19 11:24:13 EDT 2016 x86_64
Job Statistics:
Input device/file name: /dev/mapper/mpatha (device type=disk)
Type of I/O's performed: sequential (forward)
Job Information Reported: Job 1
Number of slices: 10
Data operation performed: Verified '/dev/mapper/mpatha' with '/dev/mapper/mpathb'.
Total records read: 655360
Total bytes read: 21474836480 (20971520.000 Kbytes, 20480.000 Mbytes, 20.000 Gbytes)
Total records written: 0
Total bytes written: 0 (0.000 Kbytes, 0.000 Mbytes, 0.000 Gbytes)
Total records processed: 655360 @ 32768 bytes/record (32.000 Kbytes)
Total bytes transferred: 21474836480 (20971520.000 Kbytes, 20480.000 Mbytes)
Average transfer rates: 733494714 bytes/sec, 716303.432 Kbytes/sec
Number I/O's per second: 22384.482
Number seconds per I/O: 0.0000 (0.04ms)
Total passes completed: 1/1
Total errors detected: 0/1
Total elapsed time: 00m29.28s
Total system time: 00m10.45s
Total user time: 00m42.31s
Starting time: Fri Feb 1 14:37:33 2019
Ending time: Fri Feb 1 14:38:03 2019
#

## Slide 15: Zero ROD Token to Unmap Blocks
# spt dsf=${DST} cdb='9e 12' starting=0 logprefix=
Get LBA Status Information:
Mapped Blocks: 20971520
Deallocated Blocks: 0
Total Blocks: 20971520
# spt cdb='83 11' dsf=${DST} starting=0 enable=zerorod enable=recovery,sense emit=default logprefix=
Thread: 1
Device Name: /dev/mapper/mpathb
Device Info: Block Length=512, Capacity=20971520
Block Range: 0 - 20971520
SCSI Name: XCOPY - Write Using Token
SCSI CDB: 83 11 00 00 00 00 01 8b 46 06 00 00 02 28 00 00
Data Direction: write
Data Length: 512
Exit Status: 0 = SUCCESS
Host Status: 0 = DID_OK
Driver Status: 0 = DRIVER_OK
SCSI Status: 0 = SCSI_GOOD
Sense Code: 0 = NO CODE
Sense Key: 0 = NO SENSE
asc/asq: (00, 00) = No additional sense information
Bytes Transferred: 32 (data bytes transferred)
Residual: 773 (bytes not transferred)
Iterations: 1
Total Bytes: 88320
Total Blocks: 20971520
Total Operations: 322
Sense Data: 00 00 00 00 00 00 00 00
Elapsed Time: 00m00.19s
Starting Time: Fri Feb 1 14:43:29 2019
Ending Time: Fri Feb 1 14:43:30 2019
# spt dsf=${DST} cdb='9e 12' starting=0 logprefix=
Get LBA Status Information:
Mapped Blocks: 0
Deallocated Blocks: 20971520
Total Blocks: 20971520
#

## Slide 16: SES LED Control (useful on array)
Modify SES Control Elements
Format:
  spt ses {clear|set}={devoff|fail/fault|ident/locate|unlock}
Examples:
  # export SPT_DEVICE=/dev/sg50
  # spt ses set=ident etype=array element=85
  # spt logprefix= rcvdiag etype=array element=85 page=enclosure
  Enclosure Status Diagnostic Page:
  Page Code: 0x2
  …
  Element Descriptor: 85
  Element Text: Array Slots
  Element Status Code: OK (0x01)
  …
  Identify LED: On
  …
  # spt ses clear=ident etype=array element=85

## Slide 17: Log Pages
Format:
  spt logsense page={name|code}
Examples:
  # spt logsense page=write_error logprefix= rfmt=brief
  Write Error Counter Parameters (Page 0x2 - Current Cumulative Values):
  Errors Corrected w/o Substantial Delay: 0
  Errors Corrected with Possible Delays: 8
  Total re-Reads or re-Writes: 0
  Total Errors Corrected: 8
  Times Correction Algorithm Processed: 17040
  Total Bytes Processed: 3097992679424
  Total Uncorrected Errors: 0
  #

## Slide 18: Request Sense
Provide Request Sense for In-Progress Commands
Format:
  spt requestsense
Examples:
  # spt test bextended
  # spt requestsense logprefix=
  Request Sense Data: (sense length 32 bytes)
  Error Code: 0x70 = Current Error
  Information Field Valid: No
  Sense Key: 0x2 = NOT READY
  Information Field: 0 (0)
  Additional Sense Length: 24 (0x18)
  Command Specific Information: 0 (0)
  Additional Sense Code/Qualifier: (0x4, 0x9) - Logical unit not ready, self-test in progress
  Field Replaceable Unit Code: 0
  Sense Key Specific Bytes: 80 03 08
  Progress Indication: 1.18%
  Additional Sense Bytes: 00 00 f5 05 00 00 00 00 00 00 00 00 00 00
  #

## Slide 19: Show Device Information
Show SCSI device information
Format:
  # spt show { devices| edt } [filters]
Example:
  Show Devices Filters:
device(s)=string The device path(s).
device_type(s)={value|string},...
The device type. (or dtype=)
exclude=string The exclude path(s).
product=string The product name. (or pid=)
vendor=string The vendor name. (or vid=)
revision=string The revision level. (or rev=)
fw_version=string The firmware version. (or fwver=)
serial=string The serial number.
show-fields=string Show devices brief fields. (or sflds=).
show-format=string Show devices format control. (or sfmt=).
show-path=string,... Show devices using path. (or spath=).

## Slide 20: Show Devices Example
# lsdisks --vendor Nimble
Linux SCSI Array SW Drive Block
Device Device Vendor Product Version Capacity Length Serial Number
---------- ---------- -------- ---------------- -------- ------------ ------ --------------------------------
/dev/sdj /dev/sg10 Nimble Server 5.1 20971520 512 92586db90a929ca96c9ce9004d05262d
/dev/sdl /dev/sg12 Nimble Server 5.1 20971520 512 92586db90a929ca96c9ce9004d05262d
/dev/sdn /dev/sg14 Nimble Server 5.1 20971520 512 92586db90a929ca96c9ce9004d05262d
/dev/sdp /dev/sg16 Nimble Server 5.1 20971520 512 92586db90a929ca96c9ce9004d05262d
…
/dev/sdi /dev/sg9 Nimble Server 5.1 20971520 512 7de17fd7510524536c9ce9004d05262d
/dev/sds /dev/sg19 Nimble Server 5.1 20971520 512 7de17fd7510524536c9ce9004d05262d
/dev/sdu /dev/sg21 Nimble Server 5.1 20971520 512 7de17fd7510524536c9ce9004d05262d
/dev/sdw /dev/sg23 Nimble Server 5.1 20971520 512 7de17fd7510524536c9ce9004d05262d
/dev/sdy /dev/sg25 Nimble Server 5.1 20971520 512 7de17fd7510524536c9ce9004d05262d
#

## Slide 21: Show Devices Fields Example
# spt show devices vid=Nimble show-fields='vid,serial,swver,syncrep,paths'
Vendor Serial Number SW Version Sync Rep Device Paths
-------- -------------------------------- ---------- -------- ------------
Nimble 1ab3574fff125ce66c9ce9004d05262d 5.1 False /dev/sde /dev/sg5 /dev/sdg /dev/sg7 /dev/mapper/mpathd /dev/mapper/21ab3574fff125ce66c9ce9004d05262d
Nimble 34b7a7a09b7abc1e6c9ce9004d05262d 5.1 False /dev/sdf /dev/sg6 /dev/sdh /dev/sg8 /dev/mapper/mpathe /dev/mapper/234b7a7a09b7abc1e6c9ce9004d05262d
Nimble eb17d3b14c2f1bf36c9ce9004d05262d 5.1 False /dev/sdi /dev/sg9 /dev/sdk /dev/sg11 /dev/mapper/mpathf /dev/mapper/2eb17d3b14c2f1bf36c9ce9004d05262d
Nimble 05eaa367468617896c9ce9004d05262d 5.1 False /dev/sdj /dev/sg10 /dev/sdl /dev/sg12 /dev/mapper/mpathg /dev/mapper/205eaa367468617896c9ce9004d05262d
Nimble f081af3d26bad6296c9ce9004d05262d 5.1 False /dev/sdc /dev/sg3 /dev/sdn /dev/sg14 /dev/mapper/mpathb /dev/mapper/2f081af3d26bad6296c9ce9004d05262d
Nimble c16c750ad1c5ff9a6c9ce9004d05262d 5.1 False /dev/sdd /dev/sg4 /dev/sdo /dev/sg15 /dev/mapper/mpathc /dev/mapper/2c16c750ad1c5ff9a6c9ce9004d05262d
Nimble d68d651c8052829e6c9ce9004d05262d 5.1 False /dev/sdb /dev/sg2 /dev/sdp /dev/sg16 /dev/mapper/mpatha /dev/mapper/2d68d651c8052829e6c9ce9004d05262d
Nimble a7e2da4ed76e35fe6c9ce9004d05262d 5.1 False /dev/sdm /dev/sg13 /dev/sdq /dev/sg17 /dev/mapper/mpathh /dev/mapper/2a7e2da4ed76e35fe6c9ce9004d05262d
#

## Slide 22: Show Device JSON Output Example
# spt show edt device=/dev/mapper/mpathh ofmt=json
{
"SCSI Devices": {
"Device List": [
{
"Peripheral Device Type": 0,
"Peripheral Device Type Description": "Direct Access Device",
"Vendor Identification": "Nimble ",
"Product Identification": "Server ",
"Firmware Revision Level": "1.0 ",
"Full Firmware Version": "<not available>",
"Product Serial Number": "a7e2da4ed76e35fe6c9ce9004d05262d",
"Device World Wide Name": "0xa7e2da4ed76e35fe6c9ce9004d05262d",
"Device Target Port": "<not available>",
"Array SW Version": "5.1",
"Target Type": "Volume Scoped",
"Sync Replication": false,
"Device Paths": "\/dev\/mapper\/mpathh",
"Path Types": [
{
"DMMP Device": "\/dev\/mapper\/mpathh",
"SCSI Nexus": "[27:0:0:0]"
}
]
}
],
"JSON Status": 0
}
}
#

## Slide 23: Show SCSI Sense Information
Format:
  spt show scsi [filters]
Examples:
  # spt show scsi ascq=0x0404
  Sense Code/Qualifier = (0x4, 0x4) = Logical unit not ready, format in progress
  # spt show scsi key=0x2
  Sense Key = 0x2 = NOT READY
  # spt show scsi status=28
  SCSI Status = 0x28 = SCSI_QUEUE_FULL
  #

## Slide 24: List Disks Script
Python Script Utilizing spt to List Disks/Enclosure Information
Format:
  lsdisks [options…]
Help Text:
  # lsdisks --help
  usage: lsdisks [-h] [--debug] [--drives DRIVES] [--exclude EXCLUDE] [--force_spt] [--json] [--long] [--noencs] [--noheader]
  [--power_on_hours] [--firmware_version FIRMWARE_VERSION] [--product_name PRODUCT_NAME] [--vendor_name VENDOR_NAME]
  [--serial_number SERIAL_NUMBER] [--sas_address SAS_ADDRESS] [--target_port TARGET_PORT] [--use_lsscsi]
  [--spt_path SPT_PATH]
  optional arguments:
  -h, --help show this help message and exit
  --debug The debug flag. (Default: False)
  --drives DRIVES The drives to display. (Default: [])
  --exclude EXCLUDE The drives to exclude. (Default: [])
  --force_spt Force using spt (debug). (Default: False)
  --json Enable JSON format. (Default: False)
  --long Enable long format. (Default: False)
  --noencs Exclude enclosures. (Default: False)
  --noheader Exclude headers. (Default: False)
  --power_on_hours Include power on hours. (Default: True)
  --firmware_version FIRMWARE_VERSION
  The firmware version. (Default: None)
  --product_name PRODUCT_NAME
  The product name. (Default: None)
  --vendor_name VENDOR_NAME The vendor name. (Default: None)
  --serial_number SERIAL_NUMBER
  The serial number. (Default: None)
  --sas_address SAS_ADDRESS The SAS address. (Default: None)
  --target_port TARGET_PORT The target port. (Default: None)
  --use_lsscsi Find devices via lsscsi. (Default: False)
  --spt_path SPT_PATH The spt tool path. (Default: /usr/local/bin/spt)
  #

## Slide 25: List Disks Example
# lsdisks
Linux SCSI Array SW Drive Block
Device Device Vendor Product Version Capacity Length Serial Number
---------- ---------- -------- ---------------- -------- ------------ ------ --------------------------------
/dev/sda /dev/sg0 VMware Virtual disk 83886080 512 <not available>
/dev/sde /dev/sg5 Nimble Server 5.1 20971520 512 1ab3574fff125ce66c9ce9004d05262d
/dev/sdg /dev/sg7 Nimble Server 5.1 20971520 512 1ab3574fff125ce66c9ce9004d05262d
/dev/sdf /dev/sg6 Nimble Server 5.1 20971520 512 34b7a7a09b7abc1e6c9ce9004d05262d
/dev/sdh /dev/sg8 Nimble Server 5.1 20971520 512 34b7a7a09b7abc1e6c9ce9004d05262d
/dev/sdi /dev/sg9 Nimble Server 5.1 20971520 512 eb17d3b14c2f1bf36c9ce9004d05262d
/dev/sdk /dev/sg11 Nimble Server 5.1 20971520 512 eb17d3b14c2f1bf36c9ce9004d05262d
/dev/sdj /dev/sg10 Nimble Server 5.1 20971520 512 05eaa367468617896c9ce9004d05262d
/dev/sdl /dev/sg12 Nimble Server 5.1 20971520 512 05eaa367468617896c9ce9004d05262d
/dev/sdc /dev/sg3 Nimble Server 5.1 20971520 512 f081af3d26bad6296c9ce9004d05262d
/dev/sdn /dev/sg14 Nimble Server 5.1 20971520 512 f081af3d26bad6296c9ce9004d05262d
/dev/sdd /dev/sg4 Nimble Server 5.1 20971520 512 c16c750ad1c5ff9a6c9ce9004d05262d
/dev/sdo /dev/sg15 Nimble Server 5.1 20971520 512 c16c750ad1c5ff9a6c9ce9004d05262d
/dev/sdb /dev/sg2 Nimble Server 5.1 20971520 512 d68d651c8052829e6c9ce9004d05262d
/dev/sdp /dev/sg16 Nimble Server 5.1 20971520 512 d68d651c8052829e6c9ce9004d05262d
/dev/sdm /dev/sg13 Nimble Server 5.1 20971520 512 a7e2da4ed76e35fe6c9ce9004d05262d
/dev/sdq /dev/sg17 Nimble Server 5.1 20971520 512 a7e2da4ed76e35fe6c9ce9004d05262d
#

## Slide 26: List Disks Long Format Example
# lsdisks --long --drives=/dev/sdq
Device Type: disk
Device Description: Direct Access Device
Linux Device Name: /dev/sdq
SCSI Device Name: /dev/sg17
Product Identification: Server
Vendor Identification: Nimble
Firmware Version: 1.0
Array SW Version: 5.1
Serial Number: a7e2da4ed76e35fe6c9ce9004d05262d
Drive Capacity: 20971520
Block Length: 512
#

## Slide 27: List Disks JSON Format Example
# lsdisks --long --drives=/dev/sdq --json
[
{
"SAS Address": "",
"DMMP Device Name": "",
"SCSI Device Name": "/dev/sg17",
"Product Identification": "Server",
"Drive Capacity": 20971520,
"Linux Device Name": "/dev/sdq",
"Device World Wide Name": "0xa7e2da4ed76e35fe6c9ce9004d05262d",
"Power On Hours": "",
"Device Type": "disk",
"Serial Number": "a7e2da4ed76e35fe6c9ce9004d05262d",
"Device Type Description": "Direct Access Device",
"Block Length": 512,
"Enclosure Slot": "",
"Firmware Version": "1.0",
"Enclosure Device": "",
"Vendor Identification": "Nimble",
"Revision Level": "1.0",
"Slot Description": "",
"Linux SCSI Nexus": "[27:0:0:0]",
"Current Temperature": "",
"Array SW Version": "5.1"
}
]
#

## Slide 28: List Disks on Nimble Array
rtp-afa77-A:tmp# ./lsdisks
Linux SCSI Firmware Drive Block Curr Enc SCSI Enc Enc Slot
Device Device Vendor Product Revision Capacity Length Temp Serial Number SAS Address Device Slot Description
---------- ---------- -------- ---------------- -------- ------------ ------ ---- -------------------- ------------------ ---------- ---- -----------------
/dev/sda /dev/sg1 ATA INTEL SSDSC2BB48 N2010112 937703088 512 23 C PHDV7473006T480BGN 0x56c9ce9f002da2b9 /dev/sg48 0 ArrayDevice00
/dev/sdb /dev/sg3 ATA INTEL SSDSC2BB48 N2010112 937703088 512 22 C PHDV749404B5480BGN 0x56c9ce9f002da3f9 /dev/sg48 4 ArrayDevice04
/dev/sdc /dev/sg5 ATA INTEL SSDSC2BB48 N2010112 937703088 512 23 C PHDV7473002W480BGN 0x56c9ce9f002da971 /dev/sg48 8 ArrayDevice08
/dev/sdd /dev/sg7 ATA INTEL SSDSC2BB48 N2010112 937703088 512 22 C PHDV745100A5480BGN 0x56c9ce9f002dadb1 /dev/sg48 12 ArrayDevice0C
/dev/sde /dev/sg9 ATA INTEL SSDSC2BB48 N2010112 937703088 512 22 C PHDV749404F1480BGN 0x56c9ce9f002daa09 /dev/sg48 16 ArrayDevice10
/dev/sdf /dev/sg11 ATA INTEL SSDSC2BB48 N2010112 937703088 512 22 C PHDV745000YC480BGN 0x56c9ce9f002da749 /dev/sg48 20 ArrayDevice14
/dev/sdg /dev/sg13 ATA INTEL SSDSC2BB48 N2010112 937703088 512 22 C PHDV7451003C480BGN 0x56c9ce9f002dae11 /dev/sg48 1 ArrayDevice01
/dev/sdh /dev/sg15 ATA INTEL SSDSC2BB48 N2010112 937703088 512 23 C PHDV74500195480BGN 0x56c9ce9f002da351 /dev/sg48 5 ArrayDevice05
/dev/sdi /dev/sg17 ATA INTEL SSDSC2BB48 N2010112 937703088 512 23 C PHDV74510140480BGN 0x56c9ce9f002da851 /dev/sg48 9 ArrayDevice09
/dev/sdj /dev/sg19 ATA INTEL SSDSC2BB48 N2010112 937703088 512 22 C PHDV74510038480BGN 0x56c9ce9f002daa19 /dev/sg48 13 ArrayDevice0D
/dev/sdk /dev/sg21 ATA INTEL SSDSC2BB48 N2010112 937703088 512 22 C PHDV745000YS480BGN 0x56c9ce9f002da7e9 /dev/sg48 17 ArrayDevice11
/dev/sdl /dev/sg23 ATA INTEL SSDSC2BB48 N2010112 937703088 512 22 C PHDV745101J0480BGN 0x56c9ce9f002da9c9 /dev/sg48 21 ArrayDevice15
/dev/sdm /dev/sg25 ATA INTEL SSDSC2BB48 N2010112 937703088 512 22 C PHDV7450014Q480BGN 0x56c9ce9f002db109 /dev/sg48 2 ArrayDevice02
/dev/sdn /dev/sg27 ATA INTEL SSDSC2BB48 N2010112 937703088 512 22 C PHDV747300ET480BGN 0x56c9ce9f002ddf49 /dev/sg48 6 ArrayDevice06
/dev/sdo /dev/sg29 ATA INTEL SSDSC2BB48 N2010112 937703088 512 23 C PHDV74730056480BGN 0x56c9ce9f002dada9 /dev/sg48 10 ArrayDevice0A
/dev/sdp /dev/sg31 ATA INTEL SSDSC2BB48 N2010112 937703088 512 22 C PHDV745000ZM480BGN 0x56c9ce9f002db0a1 /dev/sg48 14 ArrayDevice0E
/dev/sdq /dev/sg33 ATA INTEL SSDSC2BB48 N2010112 937703088 512 22 C PHDV7473005C480BGN 0x56c9ce9f002da6c9 /dev/sg48 18 ArrayDevice12
/dev/sdr /dev/sg35 ATA INTEL SSDSC2BB48 N2010112 937703088 512 23 C PHDV7473004F480BGN 0x56c9ce9f002dab41 /dev/sg48 22 ArrayDevice16
/dev/sds /dev/sg37 ATA INTEL SSDSC2BB48 N2010112 937703088 512 22 C PHDV7450015B480BGN 0x56c9ce9f002dade9 /dev/sg48 3 ArrayDevice03
/dev/sdt /dev/sg39 ATA INTEL SSDSC2BB48 N2010112 937703088 512 22 C PHDV7450017T480BGN 0x56c9ce9f002ddf89 /dev/sg48 7 ArrayDevice07
/dev/sdu /dev/sg41 ATA INTEL SSDSC2BB48 N2010112 937703088 512 22 C PHDV74500168480BGN 0x56c9ce9f002dac49 /dev/sg48 11 ArrayDevice0B
/dev/sdv /dev/sg43 ATA INTEL SSDSC2BB48 N2010112 937703088 512 22 C PHDV745000ZA480BGN 0x56c9ce9f002dac89 /dev/sg48 15 ArrayDevice0F
/dev/sdw /dev/sg45 ATA INTEL SSDSC2BB48 N2010112 937703088 512 22 C PHDV745000YN480BGN 0x56c9ce9f002da7b9 /dev/sg48 19 ArrayDevice13
/dev/sdx /dev/sg47 ATA INTEL SSDSC2BB48 N2010112 937703088 512 22 C PHDV747300F4480BGN 0x56c9ce9f002db051 /dev/sg48 23 ArrayDevice17
/dev/sdy /dev/sg49 ATA SQF-SM4U2-16G-9N S9FUA028 31277232 512 FEB40781040800295992
rtp-afa77-A:tmp#

## Slide 29: Test Commands
Perform a Diagnostic Test
Format:
  spt test options
  Test Options:
    abort Abort a background test.
    selftest Standard self test.
    bextended Background extended self test.
    bshort Background short self test.
    extended Foreground extended self test.
    short Foreground short self test.
Examples:
  # spt testself
  # spt test short

## Slide 30: spt Python Shared Library
Uses Python CTYPES to call spt shared library
Snippet from spt unit test script (sptp/sptut.py):
# Note: This will be packaged with spt and copied to /usr/local/bin
self.libspt = CDLL('./libspt.so')
self.sptapi = self.libspt.spt
self.program = "sptut"
#
# int
# spt(char *stdin_buffer,
# char *stderr_buffer, int stderr_length,
# char *stdout_buffer, int stdout_length,
# char *emit_status_buffer, int emit_status_length)
#
self.sptapi.restype = c_int
self.sptapi.argtypes = [c_char_p, c_char_p, c_int, c_char_p, c_int, c_char_p, c_int]
self.spt_args = {}
self.spt_args['stderr_length'] = STDERR_BUFFER_SIZE
self.spt_args['stdout_length'] = STDOUT_BUFFER_SIZE
self.spt_args['emit_status_length'] = EMIT_BUFFER_SIZE
self.spt_args['stderr_buffer'] = create_string_buffer('\000' * self.spt_args['stderr_length'])
self.spt_args['stdout_buffer'] = create_string_buffer('\000' * self.spt_args['stdout_length'])
self.spt_args['emit_status_buffer'] = create_string_buffer('\000' * self.spt_args['emit_status_length'])
self.spt_args['stdout_dict'] = None
self.spt_args['emit_dict'] = None
…
sptut.py is Multi-Threaded Script calling Threaded spt API.

## Slide 31: spt Shared Library Unit Test Script
# ./sptut.py --help
usage: sptut [-h] [--debug] [--verify]
optional arguments:
-h, --help show this help message and exit
--debug The debug flag. (Default: False)
--verify Do verify media. (Default: False)
# ./sptut.py --verify
Executing: version
Author: Robin T. Miller, Date: October 29, 2018, Version: 3.16
Executing: show devices dtype=direct
Starting thread for /dev/sda...
Executing: dsf=/dev/sda cdb=0 status=good retry=100 msleep=100 enable=wait
Starting thread for /dev/sde...
Executing: dsf=/dev/sde cdb=0 status=good retry=100 msleep=100 enable=wait
Starting thread for /dev/sdg...
Executing: dsf=/dev/sdg cdb=0 status=good retry=100 msleep=100 enable=wait
Starting thread for /dev/sdf...
Executing: dsf=/dev/sdf cdb=0 status=good retry=100 msleep=100 enable=wait
Executing: dsf=/dev/sdf inquiry
Executing: dsf=/dev/sdf readcapacity16
Executing: dsf=/dev/sdf inquiry page=serial
Executing: dsf=/dev/sdf cdb=0x8f bs=32k limit=1g threads=1
…
# spt showopcodes | fgrep -i verify | fgrep 0x8f
0x8f 0x00 none yes no 65536 Verify(16)
#

## Slide 32: SPT Roadmap
Finish adding SES diagnostic page support.
Add more Inquiry, Log, and Mode pages.
Add firmware download and Format support.
Add JSON output format for other SCSI operations.
Add SCSI compliance verification.
Add support for Linux “bsg” SCSI interface.
Add support for multiple devices. (like dt)
Job Control for waiting on Async Threads. (like dt)
Add server/client message passing using ZeroMQ.