## Slide 1: SCSI Pass-Through (SPT) UNMAPs
Robin T. Miller
December 18th, 2020
Updated September 25th, 2025

## Slide 2: Topics
Overview of UNMAPs
SCSI UNMAP Methods
Host File System Support
Futures
Notes: AI: Check presentations to see the P/E cycles for different vendors

## Slide 3: Overview of UNMAPs
Supported on Thinly Provisioned Storage
Allow arrays to efficiently reuse freed blocks
Host File Systems support via File Trim Operations
  File Trim operations converted into SCSI UNMAP commands
  Windows enables File Trims automatically for NTFS
  Linux file systems support this via the “-o discard” mount option
    verified on ext4 and XFS file systems
  Veritas supports similar via fsadm options
  File Trims triggered by freeing blocks: file delete, file truncate
Host SCSI tools exist to verify UNMAP operations on direct disks
Notes: AI: Check presentations to see the P/E cycles for different vendors

## Slide 4: SCSI UNMAP Methods
Multiple methods available:
  SCSI UNMAP command (opcode 0x42)
  Write Same 16 with unmap (opcode 0x93,0x08)
  Write Using Token (WUT) with Zero ROD (0x83,0x11)
SCSI UNMAP is the most popular method
SCSI Read Capacity(16) reports provisioning information
SCSI Get LBA Status reports mapped/deallocated blocks
SCSI Inquiry VPD Block Limits reports maximum UNMAP information
Notes: AI: Check presentations to see the P/E cycles for different vendors

## Slide 5: Report Capacity & Provisioning Type
# export SCU_DEVICE="/dev/mapper/mpathu"
# spt readcapacity16 logprefix=
Read Capacity(16) Data: (data length 32 bytes)
Maximum Capacity: 409600000 (200000.000 megabytes)
Block Length: 512
Protection Enabled: No
Protection Type: 0
Logical Blocks per Physical Exponent: 0 (1 blocks per physical)
Protection Information Exponent: 0
Logical Block Provisioning Management: Yes (Thin Provisioned)
Logical Block Provisioning Read Zeroes: Yes (unmapped blocks read as zero)
Lowest Aligned Logical Block Address: 0
#

## Slide 6: Report UNMAP Information
# spt inquiry page=block_limits logprefix=
Block Limits Page:
Peripheral Device Type: 0 (Direct Access Device)
Peripheral Qualifier: 0 (Peripheral Device Connected)
Page Code: 0xb0
Page Length: 60 (0x3c)
Write Same No Zero: False <- Note: We only support zero data!
Maximum Compare and Write Length: 1 block
Optimal Transfer Length Granularity: 0 blocks
Maximum Transfer Length: 0 blocks
Optimal Transfer Length: 0 blocks
Maximum Prefetch Transfer Length: 0 blocks
Maximum Unmap LBA Count: 2097152 blocks (1073741824 bytes)
Maximum Unmap Descriptor Count: 1
Optimal Unmap Granularity: 8 blocks
Unmap Granularity Alignment Valid: True
Unmap Granularity Alignment: 0
Maximum Write Same Length: 2097152 blocks (1073741824 bytes)
Maximum Atomic Transfer Length: 0
Atomic Alignment: 0
Atomic Transfer Length Granularity: 0
Maximum Atomic Transfer Boundary: 0
Maximum Atomic Boundary Size: 0
#

## Slide 7: Populate Disk Blocks
# spt cdb=8a starting=0 bs=256k emit=default pattern=iot slices=64 logprefix=
…
Thread: 50
Device Name: /dev/mapper/mpathu
Device Info: Block Length=512, Capacity=409600000
Block Range: 313600000 - 320000000
SCSI Name: Write(16)
SCSI CDB: 8a 00 00 00 00 00 13 12 ce 00 00 00 02 00 00 00
Data Direction: write
Data Length: 262144
Exit Status: 0 = SUCCESS
Host Status: 0 = DID_OK
Driver Status: 0 = DRIVER_OK
SCSI Status: 0 = SCSI_GOOD
Sense Code: 0 = NO CODE
Sense Key: 0 = NO SENSE
asc/asq: (00, 00) = No additional sense information
Bytes Transferred: 262144 (data bytes transferred)
Residual: 0 (bytes not transferred)
Iterations: 1
Total Bytes: 3276800000
Total Blocks: 6400000
Total Operations: 12501
Sense Data: 00 00 00 00 00 00 00 00
Elapsed Time: 01m44.75s
Starting Time: Wed Dec 16 17:30:02 2020
Ending Time: Wed Dec 16 17:31:47 2020
#

## Slide 8: Report Mapped / Deallocated Blocks
# spt getlbastatus logprefix= emit=default
Get LBA Status Information:
Mapped Blocks: 409600000
Deallocated Blocks: 0
Total Blocks: 409600000
Thread: 1
Device Name: /dev/mapper/mpathu
Device Info: Block Length=512, Capacity=409600000
Block Range: 0 - 409600000
SCSI Name: Get LBA Status(16)
SCSI CDB: 9e 12 00 00 00 00 18 60 00 00 00 00 28 a8 00 00
Data Direction: read
Data Length: 10408
Exit Status: 0 = SUCCESS
Host Status: 0 = DID_OK
Driver Status: 0 = DRIVER_OK
SCSI Status: 0 = SCSI_GOOD
Sense Code: 0 = NO CODE
Sense Key: 0 = NO SENSE
asc/asq: (00, 00) = No additional sense information
Bytes Transferred: 24 (data bytes transferred)
Residual: 10384 (bytes not transferred) <- FYI: Only one descriptor returned (spt requested 650 entries).
Iterations: 1
Total Bytes: 11544
Total Blocks: 409600000
Total Operations: 482
Sense Data: 00 00 00 00 00 00 00 00
Elapsed Time: 00m47.58s
Starting Time: Wed Dec 16 16:07:20 2020
Ending Time: Wed Dec 16 16:08:07 2020
#

## Slide 9: UNMAP Blocks
# spt unmap emit=default logprefix=
Thread: 1
Device Name: /dev/mapper/mpathu
Device Info: Block Length=512, Capacity=409600000
Block Range: 0 - 409600000
SCSI Name: Unmap
SCSI CDB: 42 00 00 00 00 00 00 00 18 00
Data Direction: write
Data Length: 24
Exit Status: 0 = SUCCESS
Host Status: 0 = DID_OK
Driver Status: 0 = DRIVER_OK
SCSI Status: 0 = SCSI_GOOD
Sense Code: 0 = NO CODE
Sense Key: 0 = NO SENSE
asc/asq: (00, 00) = No additional sense information
Bytes Transferred: 24 (data bytes transferred)
Residual: 0 (bytes not transferred)
Iterations: 1
Total Bytes: 4704
Total Blocks: 409600000
Total Operations: 198
Sense Data: 00 00 00 00 00 00 00 00
Elapsed Time: 00m00.35s
Starting Time: Wed Dec 16 16:10:33 2020
Ending Time: Wed Dec 16 16:10:33 2020
#

## Slide 10: Show Deallocated Blocks
# spt getlbastatus logprefix=
Get LBA Status Information:
Mapped Blocks: 0
Deallocated Blocks: 409600000
Total Blocks: 409600000
# spt getlbastatus logprefix= starting=1g/b limit=100g
Get LBA Status Information:
Mapped Blocks: 0
Deallocated Blocks: 209715200
Total Blocks: 209715200
#

## Slide 11: Write Same w/UNMAP
# spt cdb=8a starting=0 bs=256k pattern=iot slices=64
# spt cdb=93,08 starting=0 emit=default logprefix=
Thread: 1
Device Name: /dev/mapper/mpathu
Device Info: Block Length=512, Capacity=409600000
Block Range: 0 - 409600000
SCSI Name: Write Same(16)
SCSI CDB: 93 08 00 00 00 00 18 60 00 00 00 0a 00 00 00 00
Data Direction: write
Data Length: 512
Exit Status: 0 = SUCCESS
Host Status: 0 = DID_OK
Driver Status: 0 = DRIVER_OK
SCSI Status: 0 = SCSI_GOOD
Sense Code: 0 = NO CODE
Sense Key: 0 = NO SENSE
asc/asq: (00, 00) = No additional sense information
Bytes Transferred: 512 (data bytes transferred)
Residual: 0 (bytes not transferred)
Iterations: 1
Total Bytes: 100352
Total Blocks: 409600000
Total Operations: 197
Sense Data: 00 00 00 00 00 00 00 00
Elapsed Time: 00m00.35s
Starting Time: Wed Dec 16 16:55:50 2020
Ending Time: Wed Dec 16 16:55:50 2020
#

## Slide 12: Zero ROD Method
# spt cdb=8a starting=0 bs=256k pattern=iot slices=64
# spt zerorod emit=default logprefix=
Thread: 1
Device Name: /dev/mapper/mpathu
Device Info: Block Length=512, Capacity=409600000
Block Range: 0 - 409600000
SCSI Name: XCOPY - Write Using Token
SCSI CDB: 83 11 00 00 00 00 01 8b 51 9b 00 00 02 28 00 00
Data Direction: write
Data Length: 512
Exit Status: 0 = SUCCESS
Host Status: 0 = DID_OK
Driver Status: 0 = DRIVER_OK
SCSI Status: 0 = SCSI_GOOD
Sense Code: 0 = NO CODE
Sense Key: 0 = NO SENSE
asc/asq: (00, 00) = No additional sense information
Bytes Transferred: 552 (data bytes transferred)
Residual: 0 (bytes not transferred)
Iterations: 1
Total Bytes: 1725000
Total Blocks: 409600000
Total Operations: 3127
Sense Data: 00 00 00 00 00 00 00 00
Elapsed Time: 00m00.93s
Starting Time: Wed Dec 16 17:02:44 2020
Ending Time: Wed Dec 16 17:02:45 2020
#

## Slide 13: dt I/O and UNMAP Commands
dt UNMAP Options:
  unmap_freq=value The SCSI unmap frequency. (Def: 0)
  unmap=type The SCSI unmap type.
    Valid types are: random, unmap, write_same, zerorod
UNMAPs are done via spt commands (today)
UNMAPs are only done between passes
Options to control spt:
  spt_path=string Path to SCSI (spt) tool.
    Unix default: /usr/local/bin/spt
    Windows default: c:/tools/spt.exe
  spt_options=string Additional spt options.
Roll Your Own via:
  pass_cmd=string The per pass command to execute.
BEWARE of Linux BUG: (external commands via popen() cause false data corruptions!)
  Transient (read) corruption from linux host while running variable blocksize IO
  Workaround: Use smaller block sizes (e.g. 256k) or limit to single thread (so no outstanding I/O).

## Slide 14: DT Example with Random UNMAP Methods
# dt of=${DISK} bs=256k workload=high_validation slices=5 passes=2 limit=1g unmap=random disable=get_lba_status 2>&1 | fgrep Executing
dt (j:1 t:1): Executing: /usr/local/bin/spt dsf=/dev/mapper/mpathu cdb="93 08" starting=0 blocks=8192 limit=419430b enable=sense,recovery logprefix= 2>&1
dt (j:1 t:2): Executing: /usr/local/bin/spt dsf=/dev/mapper/mpathu cdb="83 11" starting=419430 limit=419430b enable=sense,recovery,zerorod logprefix= 2>&1
dt (j:1 t:3): Executing: /usr/local/bin/spt dsf=/dev/mapper/mpathu cdb="93 08" starting=838860 blocks=8192 limit=419430b enable=sense,recovery logprefix= 2>&1
dt (j:1 t:5): Executing: /usr/local/bin/spt dsf=/dev/mapper/mpathu cdb=0x42 starting=1677720 limit=419432b enable=sense,recovery logprefix= 2>&1
dt (j:1 t:4): Executing: /usr/local/bin/spt dsf=/dev/mapper/mpathu cdb="93 08" starting=1258290 blocks=8192 limit=419430b enable=sense,recovery logprefix= 2>&1
dt (j:1 t:2): Executing: /usr/local/bin/spt dsf=/dev/mapper/mpathu cdb="83 11" starting=419430 limit=419430b enable=sense,recovery,zerorod logprefix= 2>&1
dt (j:1 t:1): Executing: /usr/local/bin/spt dsf=/dev/mapper/mpathu cdb="83 11" starting=0 limit=419430b enable=sense,recovery,zerorod logprefix= 2>&1
dt (j:1 t:4): Executing: /usr/local/bin/spt dsf=/dev/mapper/mpathu cdb="93 08" starting=1258290 blocks=8192 limit=419430b enable=sense,recovery logprefix= 2>&1
dt (j:1 t:3): Executing: /usr/local/bin/spt dsf=/dev/mapper/mpathu cdb=0x42 starting=838860 limit=419430b enable=sense,recovery logprefix= 2>&1
dt (j:1 t:5): Executing: /usr/local/bin/spt dsf=/dev/mapper/mpathu cdb="83 11" starting=1677720 limit=419432b enable=sense,recovery,zerorod logprefix= 2>&1
#

## Slide 15: DT File Trim Operations
File Systems with File Trim API’s
  Windows DeviceIoControl() FSCTL_FILE_LEVEL_TRIM
dt File Trim Options:
  fstrim_freq=value - The file system trim frequency (in files).
  Flags:
    enable/disable=fstrim - File system trim. (Default: disabled)
  Like unmap options, applied after a full pass (between multiple passes)
Example:
  Administrator@rtp-fuji-qa32-1 /cygdrive/c/Robin
  $ c:/tools/dt of=Y:/dt.data bs=random limit=25m workload=high_validation disable=scsi,stats passes=3 enable=fdebug,fstrim logprefix=
  File name: Y:/dt.data
  DEBUG: GetFileAttributesEx failed, error 2 - The system cannot find the file specified.
  Directory: Y:, File: Y:/dt.data, Base Name: dt.data
  Requesting file system information...
  Trimming file Y:/dt.data, starting offset: 0, length: 26214400 bytes
  Trimming file Y:/dt.data, starting offset: 0, length: 26214400 bytes
  Trimming file Y:/dt.data, starting offset: 0, length: 26214400 bytes
  Deleting file Y:/dt.data...
  Administrator@rtp-fuji-qa32-1 /cygdrive/c/Robin

## Slide 16: Debugging
# spt unmap logprefix= limit=3g enable=xdebug (debug adds full SCSI debug)
Range Descriptor: 0
Number of Blocks: 2097152 (0x200000)
Starting Logical Block Address: 0 (0x0) (lba's 0 - 2097151)
Range Descriptor: 0
Number of Blocks: 2097152 (0x200000)
Starting Logical Block Address: 2097152 (0x200000) (lba's 2097152 - 4194303)
Range Descriptor: 0
Number of Blocks: 2097152 (0x200000)
Starting Logical Block Address: 4194304 (0x400000) (lba's 4194304 - 6291455)
# spt eval 2097152b
Expression Values:
Decimal: 1073741824
Hexadecimal: 0x40000000
512 byte Blocks: 2097152.000000
Kilobytes: 1048576.000000
Megabytes: 1024.000000
Gigabytes: 1.000000
Terabytes: 0.000977
#

## Slide 17: Futures
Integrate spt into dt as an I/O Behavior
  for example, iobehavior=spt
  delayed (currently) due to effort required
Note: Not likely to happen now that I’m retired.

## Slide 18: Backup Slides
FIO User Guide File Trim Options
FIO Options:
  trim_percentage=int - Number of verify blocks to discard/trim.
  trim_verify_zero=bool - Verify that trim/discarded blocks are returned as zeros.
  trim_backlog=int - Trim after this number of blocks are written.
  trim_backlog_batch=int - Trim this number of I/O blocks.